# Correlation between the various screen description options of the RenderMan Interface
## Physical display description (pixel coordinates)
### RiDisplay(RtToken name, RtToken type, RtToken mode, …): Selects the physical output device.
name:	Gives the literal name of the output device.
type:	The type of the output device like “framebuffer” and “file”.
mode:	The channels: “rgbaz”, “rgba”, “rgbz”, “rgb”, “a”, “z”. User defined channels can be specified by using the RiDisplayChannel command. Channels can be separated by a comma ',', like “rgb,z”.

The parameter list can contain an optional parameter “origin” [RtInt, RtInt] for the output (the physical image), that’s an offset [left, top] from top left to bottom right corner, measured in pixels. This origin is eventually not available if the output device is a file. The default value is [0, 0], that is the upper left corner. A special display can have standard values for width, height and pixel aspect ratio, that can be used, if RiFormat is not called. If the pixelaspect value of RiFormat is -1 the standard pixel aspect ratio of the display can be used.

Multiple displays can be chosen, if a “+” sign is the first character in name. The first display is used for default values of RiFormat. Therefore, the displays should have the same physical layout, at least have the same pixel aspect ratio.
## Display channel description
### RiDisplayChannel(RtToken channel, …): User defined mode of a display.
Inline definition of a display channel with optional parameters like filters. The channel must be a value that is present to the renderer, like “varying normal N”. The name without the type definition can then be used as part of mode in RiDisplay.
### RiFormat(RtFloat xres, RtFloat yres, RtFloat pixelaspect): Sets the dimension of the frame.
xres:	Width of the output window, measured in pixels.
yres:	Height of the output window, measured in pixels.
pixelaspect:	Pixel aspect ratio (pixelwidth/pixelheight) of the output device. A negative value can be used to get the current ratio from the physical display description (see RiDisplay).

The default values match the size and pixel ratio of the physical display. If the output device is a file or the dimensions are not known by the renderer, the defaults are somewhat implementation dependent: The values width 512 and height 384 can be found in the RI 3.1 specs and the default for the pixel aspect ratio is 1.0.
### RiFrameAspectRatio(RtFloat aspect): Sets the frame aspect ratio of the frame.
aspect:	The aspect ratio of the final image. aspect > 0.0.

The default value is: aspect = (pixelaspect * xres / yres) – aspect will match the values of RiFormat. If you choose a frame aspect ratio that does not match the display coordinates, the image coordinates will be smaller on either the bottom or the right edge – the image will not be distorted. The unused pixels will be left blank while rendering. The frame aspect ratio is the ratio that will appear at the final physical image, provided that the pixel aspect ratio (pixelaspect in RiFormat) is chosen correctly to match the one of the display. E.g., if you choose aspect = 16.0/9.0 you’ll get a 16.0/9.0 output.
## The screen coordinates of the image
### RiScreenWindow(RtFloat left, RtFloat right, RtFloat top, RtFloat bottom): Sets the screen window coordinates of the image
left:	The coordinates for the left edge of the image.
right:	The coordinates for the right edge of the image.
top:	The coordinates for the top edge of the image.
bottom:	The coordinates for the bottom edge of the image.

left <= right and bottom <= top

RiScreenWindows is used to set the screen coordinates for the extension of the front view explicitly. If the coordinates do not correspond with the frame aspect ratio, distortion will occur. The screen coordinates are are given in camera space, the front view is always in a distance of 1.0 units (positive z axis in camera space) away from the view point.

The default values for the screen coordinates are chosen in a way that their range -1.0 and 1.0 matches the larger side either left to right or bottom to top. The other range is calculated in a way that there will be no visible distortion at the final frame at the physical display.

If the image is physical wider than high:

left	= -1.0
right	= -1.0
top	= 1.0 / frameaspect
bottom	= -1.0 / frameaspect

If the image is physical higher than wide:

left	= -frameaspect
right	= frameaspect
top	= 1.0
bottom	= -1.0
### RiProjection(RtToken name, …): Appends a projection matrix to the current transformation matrix to get the camera screen projection.
name:	Type of the projection: “orthographic”, “perspective”, “null”.

The parameter list can contain an optional “fov” [RtFloat] parameter (>0, < 180.0) for the field of view of the “perspective” projection. The field of view will be used for the smaller edge of the front of the viewing frustum (screen coordinates), the angle for the larger side will be calculated according to the frame aspect ratio. If the fov is missing, the screen coordinates (either set explicitly or calculated by the frame aspect ratio) are used to calculate this angle: fov = 2 tan-1(length/2). Therefore, the default field of view for the perspective projection is 90°, if the default screen window is not changed (length=2, normally the height). The distant to the front view plane is always fixed to a value of 1.0 (positive z axis in camera space). The orthographic projection simply uses the screen coordinates for viewing. The near clipping plane is projected to z = 0.0, the far clipping plane is projected to the distance 1.0. You can use the “null” projection to use the CTM as projection matrix. The default projection is “orthographic”.
## The crop window (normalized display coordinates NDC)
### RiCropWindow(RtFloat xmin, RtFloat xmax, RtFloat ymin, RtFloat ymax): Sets the coordinates of the crop window, using normalized display coordinates (NDC)
xmin:	Minimal x coordinate (left edge)
xmax:	Maximal x coordinate (right edge)
ymin:	Minimal y coordinate (bottom edge)
ymax:	Maximal x coordinate (top edge)

0.0 <= xmin <= xmax <= 1.0 and 0.0 <= ymin <= xmax <= 1.0

Two crop windows have the property, that the images will fit together seamlessly at their x-edges if xmini = xmaxi-1 and at their y-edges if ymini = ymaxi-1. Therefore you can render images in stripes or tiles and fit them together afterwards. The coordinates are given in NDC (normalized display coordinates). NDC ranges from 0.0 to 1.0 in two dimensions and map to the screen coordinates.
## Literature
- Pixar Animation Studios, Pixar's RenderMan Users's Manual https://renderman.pixar.com/forum/docs/RfM_1.0/RenderMan_Manual/users_guide/index.php
- Pixar Animation Studios, PhotoRealistic RenderMan Application Note #10, The Viewing Transformation https://renderman.pixar.com/forum/docs/RfM_1.0/RenderMan_Manual/AppNotes/appnote.10.php
- Upstill, Steve: The RenderMan Companion, Addison-Wesley Professional, 1990, ISBN 978-0201508680
- Apodaca, Anthony A.; Gritz, Larry: Advanced RenderMan, Morgan Kaufmann, 1999, ISBN 978-1558606180

RenderMan® is a registered trademark of Pixar.