# Correlations Between the Various Screen Description Options of the RenderMan Interface
Memo for RiCPP, Andreas Pidde, 17th March 2008
## Physical Display Description
### RiDisplay(RtToken name, RtToken type, RtToken mode, …): Selects the physical output device.
name:	Gives the literal name of the output device.
type:	The type of the output device like “framebuffer” and “file”.
mode:	The channels: “rgbaz”, “rgba”, “rgbz”, “rgb”, “a”, “z”. User defined channels can be specified by using the RiDisplayChannel command. Channels can be separated by a comma, like “rgb,z”.

The parameter list can contain an optional parameter “origin” [RtInt, RtInt] for the output (the physical image), that’s an offset [left, top] from the top left to the bottom right corner, measured in pixels. This origin is eventually not available if the output device is a file. The default value is [0, 0], that is the upper left corner. A special display can have standard values for width, height and pixel aspect ratio, that can be used, if RiFormat is not called. If the pixelaspect value of RiFormat is less than zero the standard pixel aspect ratio of the output device used (if known).

Multiple displays (secondary displays) can be chosen, if a “+” sign is the first character in name. The first display is used for default values of RiFormat. Secondary displays can be used for arbitrary output variables.
## Display Channel Description
### RiDisplayChannel(RtToken channel, …): User defined mode (Arbitrary Output Variables AOV) of a display.
Inline definition of a display channel with optional parameters like filters. The channels can be values that are present to the renderer, like “varying normal N”. The data can be provided by shaders, that use the channel variables as output – in a way like you provide the surface color Cs by surface shaders. The name without the type definition can then be used as part of mode in RiDisplay. If you don't use the optional parameters – like an appropriate quantization, you can alternatively simply RiDeclare the display channels. Parameters can also go to the parameter list of a secondary display. The RiDisplayChannel parameters binding is stronger than that of RiDisplay.
### RiFormat(RtFloat xres, RtFloat yres, RtFloat pixelaspect): Sets the dimension of the frame (“raster” space).
xres:	Width of the output window, measured in pixels.
yres:	Height of the output window, measured in pixels.
pixelaspect:	Pixel aspect ratio (pixelwidth/pixelheight) of the output device. A negative value can be used to get the current ratio from the physical display description (see RiDisplay).

The default values match the size and pixel ratio of the physical display. If the output device is a file or the dimensions are not known by the renderer, the defaults are somewhat implementation dependent: The values width 512 and height 384 can be found in the RI 3.1 specs and the default for the pixel aspect ratio is 1.0. That's a frame aspect ratio of 4/3.
### RiFrameAspectRatio(RtFloat aspect): Sets the frame aspect ratio of the frame.
aspect:	The aspect ratio of the final image. aspect > 0.0.

The default value is: aspect = (pixelaspect * xres / yres). aspect will match the values of RiFormat. If you choose a frame aspect ratio that does not match the display coordinates, the image coordinates will be smaller on either the bottom or the right side – but the image will not be distorted. The unused pixels will be left blank while rendering. The frame aspect ratio is the ratio that will appear at the final physical image, provided that the pixel aspect ratio (pixelaspect in RiFormat) is chosen correctly to match the one of the display. If you choose aspect = 16.0/9.0 for example, you’ll get a 16.0/9.0 output.
### RiCropWindow(RtFloat xmin, RtFloat xmax, RtFloat ymin, RtFloat ymax): Sets the coordinates of the crop window, using normalized display coordinates (“NDC” space)
xmin:	Minimal x coordinate (left edge)
xmax:	Maximal x coordinate (right edge)
ymin:	Minimal y coordinate (bottom edge)
ymax:	Maximal x coordinate (top edge)

0.0 <= xmin <= xmax <= 1.0 and 0.0 <= ymin <= xmax <= 1.0

Two crop windows have the property, that the images will fit together seamlessly at their x-edges if xmini = xmaxi-1 and at their y-edges if ymini = ymaxi-1. Therefore, you can render images in stripes or tiles and fit them together afterwards. The coordinates are given in NDC (normalized display coordinates). NDC ranges from 0.0 to 1.0 in two dimensions and there are mappings to the raster space as well as to the screen window. Like in raster space and unlike screen space, the origin is located at the upper left corner of the frame, positive x axis is to the right and positive y axis is down.
## The Screen Coordinates of the Image
### RiScreenWindow(RtFloat left, RtFloat right, RtFloat top, RtFloat bottom): Sets the screen window coordinates of the image (“screen” space)
left:	The coordinates for the left edge of the image.
right:	The coordinates for the right edge of the image.
top:	The coordinates for the top edge of the image.
bottom:	The coordinates for the bottom edge of the image.

left <= right and bottom <= top

RiScreenWindows is used to set up the screen coordinates for the extension of the front view explicitly. If the coordinates do not correspond with the frame aspect ratio, distortion will occur. The screen coordinates are given in camera space. The distance of the screen window from camera position defaults to 1.0 unit.

The default values for the screen coordinates are chosen in a way that the range -1.0 and 1.0 matches the smaller side, either left to right or bottom to top. The other range is calculated in a way that there will be no visible distortion at the final frame at the physical display.

If the image is physically wider than high:

left	= -frameaspect
right	= frameaspect
top	= 1.0
bottom	= -1.0

If the image is physically higher than wide:

left	= -1.0
right	= -1.0
top	= 1.0 / frameaspect
bottom	= -1.0 / frameaspect
## The Camera to Screen Projection
### RiProjection(RtToken name, …): Appends a projection matrix to the current transformation matrix to get the camera to screen projection.
name:	Type of the projection: “orthographic” (default), “perspective”, “null”.

The parameter list can contain an optional “fov” [RtFloat] parameter (> 0, < 180.0) for the field of view of the “perspective” projection. The field of view will be used to calculate the distance of the viewing plane to the camera. If the fov is set by the user, the viewing plane is moved appropriately in z, in a way that fov matches the -1 to 1 square in screen coordinates: distance = 1 / tan(fov/2). The default is 90 degree for fov, that's a distance of 1 unit. The screen window is than positioned on that plane. The angle of the rays from viewing point through the edges of the screen window may be another angle than the one given by fov.
The orthographic projection simply uses the screen coordinates for viewing. The near clipping plane is projected to z = 0.0, the far clipping plane is projected to the distance 1.0. You can use the “null” projection to use the CTM as projection matrix. The default projection is “orthographic”. The CTM is reseted to identity for camera placement after work is done.
### RiClipping(RtFloat near, RtFloat far): Sets the near and far clipping planes (“camera” space).
The near clipping plane must be in front of the viewing point. The default values are RI_EPSILON for the near and RI_INFINITY for the far clipping plane. If possible, you should take more reasonable values. Put the near clipping farer away relaxes the problem of the maximum eye splits in REYES, a nearer far clipping plane may result in a better resolution for depth values.
## Calculating the ranges
Since options can be written in any order, the ranges for raster space and screen window can be calculated late at RiWorldBegin.

// Pseudo code to get the display options

originout = {0, 0};
xresout = 512;
yresout = 384;
pixelaspectout = 1.0;

if ( RiDisplay has been called ) {
if ( display got standard ranges ) {
xresout = width_of_display;
yresout = height_of_display;
}
if ( display got standard pixel aspect ratio ) {
pixelaspectout = pixel_aspect_ratio_of_display;
}
if ( origen parameter is available ) {
originout = origin_of_display;
}
}

if ( RiFrame has been called ) {
xresout = xres_of_RiFrame;
yresout = yres_of_RiFrame;
if ( pixelaspect_of_RiFrame > 0 ) {
pixelaspectout = pixelaspect_of_RiFrame;
}
}

frameaspectout = (RtFloat)xresout/(RtFloat)yresout;

if ( RiFrameAspect has been called ) {
frameaspectout = frameaspect_of_RiFrameAspect;
}

if ( frameaspectout >= 1.0 ) {
leftout = -frameaspectout;
rightout = frameaspectout;
bottomout = -1.0;
topout = 1.0;
} else {
leftout = -1.0;
rightout = 1.0;
bottomout = -1.0/frameaspectout;
topout = 1.0/frameaspectout;
}

if ( RiScreenWindow has been called ) {
leftout = left_of_RiScreenWindow;
rightout = right_of_RiScreenWindow;
topout = top_of_RiScreenWindow;
bottomout = bottom_of_RiScreenWindow;
}

Projectionout = “orthographic”;
ViewingPlaneDistanceout = 1.0;

if ( RiProjection has been called ) {
Projectionout = projection_of_RiProjection;
if ( projection_of_RiProjection is “perspective” ) {
fov = 90.0;
if ( fov is set by RiProjection ) {
fov = fov of RiProjection;
}
Set ViewingPlaneDistanceout appropriately to fov: 1/tan(fov/2);
}
}

Set cropwindowout to {0,0}, {1, 1};

if ( RiCropWindow has been called ) {
cropwindowout = cropwindow_of_RiCropWindow;
}

Set the clipping planes and viewing volume;
Calculate the viewing matrices;
## Literature
- Pixar Animation Studios, Pixar's RenderMan Users's Manual https://renderman.pixar.com/forum/docs/RfM_1.0/RenderMan_Manual/users_guide/index.php
- Pixar Animation Studios, PhotoRealistic RenderMan Application Note #10, The Viewing Transformation https://renderman.pixar.com/forum/docs/RfM_1.0/RenderMan_Manual/AppNotes/appnote.10.php
- Upstill, Steve: The RenderMan Companion, Addison-Wesley Professional, 1990, ISBN 978-0201508680
- Apodaca, Anthony A.; Gritz, Larry: Advanced RenderMan, Morgan Kaufmann, 1999, ISBN 978-1558606180
- Raghavachary, Saty: Rendering for Beginners, Focal Press, 2004, ISBN 978-0240519357

RenderMan® is a registered trademark of Pixar.